## Slide 1
Optic Disc and Fovea Detection
using Classical Image Processing
Delfin Aksu

## Slide 2
Why Optic Disc and Fovea?
  Optic Disc (OD) → entry point of vessels
  Fovea → center of vision
  Critical for:
    Glaucoma
    Diabetic Retinopathy
Accurate localization is essential

## Slide 3
Dataset: IDRiD
  Fundus retinal images
  Resolution: 4288 × 2848
Used subsets:
  Localization → OD & Fovea coordinates
  Segmentation → OD masks

## Slide 4
Preprocessing Pipeline
Resize
Color chanel Separation
CLAHE(Contrast Enhancement
Gaussian Smoothing

## Slide 5
Resize
All images resized to 512 × 512
Reasons:
Faster processing
Consistent filter behavior
Suitable structure scale

## Slide 6
Red channel → brightness info
Green channel → best vessel contrast
Blue channel → noisy
✔ Final choice:
Green channel used for vessel-based processing
Color Chanel Analysis

## Slide 7
Contrast Enhancement (CLAHE)
Solves uneven illumination
Works locally (tiles)
Prevents noise amplification
✔ Result:
Improves vessel & optic disc visibility

## Slide 8
Gaussian Smoothing
Removes noise & small artifacts
σ = 6 used
Produces smooth illumination map
⚠ Problem: Also removes vessel details

## Slide 9
Unsharp Masking
Restores lost vessel details
Formula:
sharpened = original + k(high-frequency)
✔ Result:
Smooth background + clear vessels

## Slide 10
Optic Disc Center Detection
Challenging due to:
  Similar bright lesions
  Vessel structures
  Illumination variations

## Slide 11
Optic Disc Localization Pipeline
Multi-step classical approach
Uses multiple feature maps:
  Brightness
  Vessel density
  Lesion suppression (penalty)
  Anatomical prior
Final decision based on fused score map
Instead of relying on a single feature, combine multiple feature maps to make the detection more robust.

## Slide 12
Field Mask Construction
Removes black background
Keeps only retinal region
Steps:
  Thresholding
  Hole filling
  Noise removal

## Slide 13
Multi-scale Brightness Maps
Captures local details and highlights small bright regions
Captures global structure and emphasize overall brightness

## Slide 14
Adaptive Percentile Threshold
  Top 5% brightest pixels selected
  produces candidate regions for optic disc
! Image-specific threshold

## Slide 15
Bright Candidate Cleanup
Morphological opening
Remove small regions
Keep plausible disc candidates

## Slide 16
Vessel Enhancement (Unsharp Masking)
Restore vessel details
High-frequency enhancement
Improves vessel detection

## Slide 17
Multi-orientation Vessel Detection
Bottom-hat filtering
12 orientations detect vessels in all directions
Each orientation captures vessels aligned with that direction, and we combine them using a pixel-wise maximum.

## Slide 18
Vessel Density Map
Disc has highest vessel density
Disk kernel convolution
Peak indicates OD region
Disk-kernel convolution of the binary vessel map. The kernel size matches the expected optic disc area, so the convolution peaks at the disc center.
bright area => more vessels
dark area => less vessel

## Slide 19
Lession Penalty
Removes bright lesions (false positives)
White top-hat
Penalizes isolated bright spots

## Slide 20
Score Fusion
Combine all features:
Brightness
Vessel density
Anatomical prior
Lession Penalty

## Slide 21
Final Detection
Optic Disc Detection
Connected component analysis
Best region selected

## Slide 22
Optic Disc Segmentation
Segmentation Pipeline
ROI extraction
Vessel removal
Adaptive thresholding
Morphological refinement
Component selection

## Slide 23
ROI Extraction
Region of Interest (ROI)
Focus on 160×160 region
Centered at detected OD
Reduces noise and computation
reduce the problem to a small region

## Slide 24
Vessel Removal
Vessels create dark artifacts
Mask + inpainting used
Produces smooth disc region

## Slide 25
Adaptive Thresholding
Otsu + Percentile
Robust to intensity variations
Final mask from max threshold

## Slide 26
Mask Refinement
  Close → fill gaps
  Fill holes
  Open → smooth boundary

## Slide 27
Final Component Selection
Multiple regions may exist
Select closest to OD center
Final disc mask

## Slide 28
Final Result

## Slide 29
Fovea Detection

## Slide 30
Anatomical Constraints
  152 pixels horizontal from OD
  25 pixels below OD
  Always on temporal side
Search Window
  140×140 window around expected position
  Reduces false detections
  Focused search

## Slide 31
Anatomical Constraints
  Fovea = darkest region
  Image inverted
  Gaussian smoothing applied

## Slide 32
Distance Prior
  Gaussian prior centered at expected position
  Penalizes far regions
  Encodes anatomical knowledge

## Slide 33
Score Fusion
Combine Darkness Map and Distance Prior
foveaScore = 0.45 * darkMap + 0.55 * distancePrior

## Slide 35
Evaluation Metric
F-score and Success Rate
Localization (OD & Fovea):
Error = Euclidean distance between predicted and ground truth centers
A prediction is correct if error < 40 px
Success Rate = correct predictions / total
Segmentation (OD):
Dice coefficient used
Measures overlap between prediction and ground truth

## Slide 36
Experimental Study
Tested key parameters:
  Threshold percentile
  Vessel weight
  Lesion weight
  Threshold ↑ → performance ↑ (MOST IMPORTANT)
  Best value: 0.99
  Vessel weight → slightly harmful
  Lesion penalty → no effect

## Slide 37
Performance Improvement
The improvement comes from tuning the adaptive threshold from 0.95 to 0.99

## Slide 38
Final Performance

## Slide 40
Teşekkür ederim.
Delfin Aksu